## Slide 1: Image Processing using Raspberry Pi

## Slide 2: The team
Harshith J – 1BM14EC035
Balaji Gorental – 1BM14EC034
Diganth P – 1BM14EC028
Dheeraj Kamath – 1BM14EC027

## Slide 3: Contents
01
Project Overview
02
Setting up the raspberry pi
03
Image Processing
04
Results

## Slide 4: Project Overview
What you can expect...
1

## Slide 5: The Plan
Raspberry Pi
Obtain Marker
Image
Aruco Marker
Marker ID
Perform Image Processing
Final Result

## Slide 6: Topics Covered
Image Processing using Python
Linux Environment
Socket Programming
Hamming Algorithm
Barcode decoding mechanism

## Slide 7: Setting up the Raspberry Pi
Let’s begin…
2

## Slide 8: Components Required
HDMI Cable
Monitor
Keyboard
Mouse
Sd card
D-Link Wi-Fi Adapter

## Slide 9: The Linux Environment
The Raspberry Pi (raspi) is based on the Linux OS. Following are the basic commands used:
sudo – for admin rights
nano – interface
cd (directory path) – For changing into another directory
chmod – creating new files
lsusb – to check devices connected to the raspi
ifconfig – for obtaining the ip address and other networking parameters

## Slide 10: The Setup Flow
On start, the raspi goes through the following steps:
prompts for username and password
enter pi for username and raspberry for password
configure the settings as per requirement
type startx to launch the GUI
use Lx Terminal for further instructions or commands
use Python for the interfacing of the pi with other components.

## Slide 11: Image Processing
Understanding various image processing terminolgies…
3

## Slide 12: Image Processing in Python
The opencv (Computer Vision) library imported into Python is used for all the image processing programs.
The functions mainly used are:
cv2.threshold()
cv2.cvtColor()
cv2.findContours()
cv2.arcLength()
cv2.approxPolyDp()
Other morphological and transformational functions will be used too.

## Slide 13: Thresholding
If pixel value is greater than a threshold value, it is assigned one value (may be white), else it is assigned another value (may be black).

## Slide 14: Contours
Contours can be explained simply as a curve joining all the continuous points (along the boundary), having same color or intensity.

## Slide 15: Approx Poly DP
Returns the coordinates of the boundary points.
(1100, 100)
(1100, 1100)
(100, 1100)
(100, 100)

## Slide 16: Aruco Markers
An ArUco marker is a synthetic square marker composed by a wide black border and a inner binary matrix which determines its identifier (id).

## Slide 17: Aruco Markers Breakdown
It is a 5x5 grid that is black and white in color.
In the grid:
the first, third and fifth columns represent parity bits.
The second and fourth columns represent the data bits.
Hence, there are ten total data bits. So the maximum number of markers that can be encoded are-
2^10 = 1024
Applications include Augmented Reality.

## Slide 18: The Coding Technique
Step 1 : Extract the ArUco from the image.

## Slide 19: The Coding Technique
Step 2 : Remove the extra padding.

## Slide 20: The Coding Technique
Step 3 : Divide the resulting image into a 5x5 grid and check the color in each cell of the second and fourth columns(in that order) in a top to bottom manner.
1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0

## Slide 21: The Coding Technique
Step 4 : If the color is white, write 1; else, write it 0.
Step 5 : The resulting number will be in binary. Convert it into decimal
This is how the id of the marker is determined.

## Slide 22
The final python code is defined using two functions:
arucoExtract(img) – Returns the required marker portion from the image
arucoDecode(marker_img) – Takes the marker image and returns the marker id

## Slide 24: Results
Be prepared to be amazed…
4

## Slide 25
Extracted Marker Image
Resized Marker Image
Final Output
👆👉👍👤👦👧👨👩👪💃🏃💑❤😂😉😋😒😭👶😸🐟🍒🍔💣📌📖🔨🎃🎈🎨🏈🏰🌏🔌🔑

## Slide 26: Applications
Used in Augmented Reality

## Slide 27
THANKS!
Any questions?
You can find me at @dheerajkamath22@gmail.com